## Slide 1: Two-Stage vs. Multi-Stage Adaptive Robust Transmission Expansion Planning
Shahab Dehghan, Nima Amjady, Antonio Conejo
Technical University of Denmark

## Slide 2: Outline
Transmission Expansion Planning (TEP): Overview
Two-Stage vs. Multi-Stage Adaptive Robust TEP
Deriving a Tractable Multi-Stage Adaptive Robust TEP
Case Study
Conclusions

## Slide 3: Outline
Transmission Expansion Planning (TEP): Overview
Two-Stage vs. Multi-Stage Adaptive Robust TEP
Deriving a Tractable Multi-Stage Adaptive Robust TEP
Case Study
Conclusions

## Slide 4: Transmission Expansion Planning
Static Models
Dynamic Models
What type of new lines?
Where?
What type of new lines?
Where?
When?
Lower computation time and accuracy!
Higher computation time and accuracy!
G. Latorre, R. D. Cruz, J. M. Areiza, and A. Villegas, “Classification of publications and models on transmission expansion planning,” IEEE Trans. Power. Syst., vol. 18, no. 2, pp. 938 – 946, May 2003.

## Slide 5: Assumptions
TEP Model
The uncertainty of load demands and wind power productions are considered.
The DC power flow equations are considered.
The single-period (static) and multi-period (dynamic) models are considered.
A Mixed-Integer Linear Programming (MILP) Problem

## Slide 6: Outline
Transmission Expansion Planning (TEP): Overview
Two-Stage vs. Multi-Stage Adaptive Robust TEP
Deriving a Tractable Multi-Stage Adaptive Robust TEP
Case Study
Conclusions

## Slide 7: Two-Stage Adaptive Robust TEP
1st Stage:
Investment decisions
(here-and-now)
Single-period Planning Horizon
Uncertainty Set:
2nd Stage:
operation decisions
(wait-and-see)

## Slide 8: Multi-Stage Adaptive Robust TEP
1st Stage:
Investment decisions
(here-and-now)
Multi-period Planning Horizon
Uncertainty Set:
3rd Stage:
operation decisions
(wait-and-see)
2nd Stage:
Investment & operation decisions
(wait-and-see)

## Slide 9: Outline
Transmission Expansion Planning (TEP): Overview
Two-Stage vs. Multi-Stage Adaptive Robust TEP
Deriving a Tractable Multi-Stage Adaptive Robust TEP
Case Study
Conclusions

## Slide 10: Problem Formulation
s.t.
Auxiliary variable
Investment variable
Independent operation variable
Dependent operation variable
Uncertain parameter
This problem is intractable due to universal quantifier for 𝝃!
We need a tractable robust counterpart…
Infinite space

## Slide 11: Step 1: Using Decision Rules
Deriving a tractable robust counterpart
where
Vector of Uncertain parameters from stage 1 to stage t
Linear Decision Rule

## Slide 12: Step 1: Using Decision Rules
Deriving a tractable robust counterpart
where
Vector of Uncertain parameters from stage 1 to stage t
Vector of step-wise 0/1 constant functions of uncertain parameters from stage 1 to stage t with
Binary Decision Rule

## Slide 13: Illustrative Example…
Deriving a tractable robust counterpart
0
2
4
1
= 2
=
Uncertainty Set:

## Slide 14: What is ?
where
Deriving a tractable robust counterpart
is component of vector that is divided into subintervals using equidistant breakpoints, i.e., .

## Slide 15: Reformulation…
Deriving a tractable robust counterpart
s.t.
BDR
LDR
This problem is still intractable due to universal quantifier for 𝝃!

## Slide 16: Step 2: Mapping to Higher Dimension
Deriving a tractable robust counterpart
Mapping…
Projection Matrices

## Slide 17: Step 2: Mapping to Higher Dimension
Deriving a tractable robust counterpart
Mapping…
or
Uncertainty Set:
Lifted Uncertainty Set:

## Slide 18: Reformulation…
Deriving a tractable robust counterpart
s.t.
BDR
LDR
This problem is still intractable due to universal quantifier for !
is discontinuous, non-linear, and non-convex.

## Slide 19: Step 3: Searching the Convex Hull of
The optimal solution of the proposed model can be obtained by searching the convex hull of the lifted uncertainty set.
The convex hull of the lifted uncertainty set can be constructed by means of:
  The extreme points of the lifted uncertainty set (i.e., )
  The one-side limits of the lifted uncertainty set (i.e., )
Deriving a tractable robust counterpart

## Slide 20: Illustrative Example…
Deriving a tractable robust counterpart
0
2
4
1
= 2
Uncertainty Set:
=
Uncertainty Subsets:
Extreme Points:
()
One-Side Limits:
()
,
,

## Slide 21: Illustrative Example…
Deriving a tractable robust counterpart
0
2
4
1
= 2
Convex Hull:

## Slide 22: Reformulation…
Deriving a tractable robust counterpart
s.t.
BDR
LDR
This problem is still intractable due to universal quantifier for !
is continuous, linear, and convex.

## Slide 23: Step 4: Using Duality Theory
Deriving a tractable robust counterpart
Generic Form of Convex Hull:
Proposition: (*) and (**) are equivalent.
(*)
(**)
Dual Variable

## Slide 24: Reformulation…
A tractable robust counterpart is derived!
s.t.

## Slide 25: Outline
Transmission Expansion Planning (TEP): Overview
Two-Stage vs. Multi-Stage Adaptive Robust TEP
Deriving a Tractable Multi-Stage Adaptive Robust TEP
Case Study
Conclusions

## Slide 26: Case Study
Characteristics of the modified Garver 6-bus test system:
  10 thermal units
  6 existing lines
  30 candidate lines
  50 MW wind farm at bus 5
  The patterns of load demands and wind power productions of ERCOT during the year 2016 are used to obtain operating conditions for a 5-year planning horizon.
The budget of uncertainty can vary between [0,6] since this test system includes 5 load demands and 1 wind farm.

## Slide 27: Optimal Solution vs. Budget of Uncertainty
CPU Time (s) | Total Cost (M$) | Lines Built |  |  |  |  | 
 |  | 5th Year | 4th Year | 3rd Year | 2nd Year | 1st Year | 
332.56 | 263.29 | - | - | - | (3-5) | 2(2-6), (3-5), 2(4-6) | 1
514.40 | 333.21 | (1-5) | (2-3) | - | - | 2(2-6),2(3-5),2(4-6) | 2
759.72 | 341.76 | - | (2-3),(1-5) | - | - | 2(2-6),2(3-5),2(4-6) | 3
784.24 | 341.76 | - | (2-3),(1-5) | - | - | 2(2-6),2(3-5),2(4-6) | 4
801.25 | 341.76 | - | (2-3),(1-5) | - | - | 2(2-6),2(3-5),2(4-6) | 5
824.13 | 341.76 | - | (2-3),(1-5) | - | - | 2(2-6),2(3-5),2(4-6) | 6
CPU Time (s) | Total Cost (M$) | Lines Built |  |  |  |  | 
 |  | 5th Year | 4th Year | 3rd Year | 2nd Year | 1st Year | 
332.56 | 263.29 | - | - | - | (3-5) |  | 1
514.40 | 333.21 | (1-5) | (2-3) | - | - |  | 2
759.72 | 341.76 | - | (2-3),(1-5) | - | - |  | 3
784.24 | 341.76 | - | (2-3),(1-5) | - | - |  | 4
801.25 | 341.76 | - | (2-3),(1-5) | - | - |  | 5
824.13 | 341.76 | - | (2-3),(1-5) | - | - |  | 6
1 breakpoint and 5 operating conditions is considered.

## Slide 28: Optimal Solution vs. Number of Breakpoints
CPU Time (s) | Total Cost (M$) | Lines Built |  |  |  |  | 
 |  | 5th Year | 4th Year | 3rd Year | 2nd Year | 1st Year | 
784.24 | 341.76 | - | (2-3),(1-5) | - | - | 2(2-6),2(3-5),2(4-6) | 1
927.15 | 340.49 | - | 2(2-3),(1-5) | - | - | 2(2-6),2(3-5),2(4-6) | 2
1023.03 | 338.80 | - | 2(2-3),(1-5) | - | - | 2(2-6),2(3-5),2(4-6) | 3
CPU Time (s) | Total Cost (M$) | Lines Built |  |  |  |  | 
 |  | 5th Year | 4th Year | 3rd Year | 2nd Year | 1st Year | 
784.24 | 341.76 | - | (2-3),(1-5) | - | - |  | 1
927.15 | 340.49 | - |  | - | - |  | 2
1023.03 | 338.80 | - |  | - | - |  | 3
= 3 and 5 operating conditions is considered.

## Slide 29: Optimal Solution vs. Number of Operating Conditions
CPU Time (s) | Total Cost (M$) | Lines Built |  |  |  |  | 
 |  | 5th Year | 4th Year | 3rd Year | 2nd Year | 1st Year | 
784.24 | 341.76 | - | (2-3),(1-5) | - | - | 2(2-6),2(3-5),2(4-6) | 5
898.95 | 340.76 | (1-5) | - | (2-3) | - | 2(2-6),2(3-5),2(4-6) | 10
934.34 | 339.55 | (2-3),(1-5) | (2-3) | - | - | 2(2-6),2(3-5),2(4-6) | 15
CPU Time (s) | Total Cost (M$) | Lines Built |  |  |  |  | 
 |  | 5th Year | 4th Year | 3rd Year | 2nd Year | 1st Year | 
784.24 | 341.76 | - | (2-3),(1-5) | - | - |  | 5
898.95 | 340.76 | (1-5) | - | (2-3) | - |  | 10
934.34 | 339.55 | (2-3),(1-5) | (2-3) | - | - |  | 15
= 3 and 1 breakpoint is considered.

## Slide 30: Two-Stage vs. Multi-Stage Robust Optimization
= 3 and 1 breakpoint is considered.
Reduction in Total Costs (M$) |  | Total Costs (M$) |  |  | 
LMMR-TEP – MTR-TEP | LMMR-TEP – STR-TEP | LMMR-TEP*** | MTR-TEP** | STR-TEP* | 
0 | 23.64 | 263.29 | 263.29 | 286.93 | 0.0
0.22 | 30.03 | 304.35 | 304.57 | 334.38 | 0.5
12.76 | 48.76 | 333.21 | 345.97 | 381.97 | 1.0
15.71 | 53.40 | 338.97 | 354.68 | 392.37 | 1.5
17.23 | 54.86 | 341.76 | 358.99 | 396.62 | 2.0
Reduction in Total Costs (M$) |  | Total Costs (M$) |  |  | 
LMMR-TEP – MTR-TEP | LMMR-TEP – STR-TEP | LMMR-TEP*** | MTR-TEP** | STR-TEP* | 
0 | 23.64 | 263.29 | 263.29 | 286.93 | 0.0
0.22 | 30.03 | 304.35 | 304.57 | 334.38 | 0.5
12.76 | 48.76 | 333.21 | 345.97 | 381.97 | 1.0
15.71 | 53.40 | 338.97 | 354.68 | 392.37 | 1.5
17.23 | 54.86 | 341.76 | 358.99 | 396.62 | 2.0
*Static Two-Stage Robust TEP: STR-TEP
**Multi-year Two-Stage Robust TEP: MTR-TEP
***Lifted Multi-year Multi-stage Robust TEP: LMMR-TEP

## Slide 31: Outline
Transmission Expansion Planning (TEP): Overview
Two-Stage vs. Multi-Stage Adaptive Robust TEP
Deriving a Tractable Multi-Stage Adaptive Robust TEP
Case Study
Conclusions

## Slide 32: Conclusions
Increasing the budget of uncertainty leads to a higher robustness against different realizations of loads and wind power productions at the expense of higher total costs.
Increasing the number of breakpoints leads to a more accurate modeling of the binary decision rules.
Increasing the number of operating conditions leads to a more accurate modeling of the patterns of loads and wind power productions.
The proposed multi-year multi-stage adaptive robust TEP model is accurate than both the single-year and multi-year two-stage adaptive robust TEP models.